## Slide 1: Portable Shower Seat
B-32
Aidan Mountain
Cem Kiyik
Fred Xu
Paul Xu
Yuning Xia

## Slide 2: Abstract
Problem Definition
Customer Needs
Target Specification
Benchmarking
Prototype 1
Prototype 2
Prototype 3
Feasibility
BOM
Business Model
Economic Report
Decision Made
Trials and Tribulations
Lessons Learned
Project Plan
Future Work
Conclusion

## Slide 3: Defining the Problem
The client is a man with impaired movement of his legs.
He is a current user of a non-portable shower seat.
He would like a seat to use when he is traveling using aircraft.
Problem Statement: Darcy (client) needs a foldable and lightweight shower seat for travelling. This shower seat must be made for wet conditions and have durable feet, and it should be under 5 lbs. and 21 inches tall.

## Slide 4: Client Needs
Comfort
Safety
Waterproof/Self draining
Number | Needs | Importance
1 | The product is 21 inches high (53 centimeter). | 1
2 | The product has a soft backrest and cushioning. | 2
3 | The product holds 250 pounds (113 kilograms). | 2
4 | The product is light weight (under 5 lbs.). | 1
5 | The product can be folded. | 2
6 | The product has durable handle and feet. | 2
7 | The product is suitable and adjustable. | 1
8 | The product is waterproof and has a drainage system. | 3
9 | The product has no latex materials. | 3

## Slide 5: Target Specification
Functional Requirements | Constraints | Non-Functional Requirements
Waterproof | Yes | < 1 min to set up
Foldable | Yes | ≥ 5 years of product life
Durable Feet | Yes | White
Height | ≥ 21 inches | 
Weight | < 5 lbs | 
Weight Hold | > 250 lbs | 
Cost | < $100 | 

## Slide 6: Benchmarking
PCP Foam Padded Bath Safety Seat
Sturdy
Large
Adjustable
Adjustable Safety Bathtub & Shower Seat
Medium Size
Inexpensive
Adjustable
Lightweight Suspended Bath Seat
Small
Limited Use
Stable

## Slide 7: Prototype 1
The first concept:
Pressure fit
Back and arm rests
Holes for water flow
Issues:
Back and arm rests are unnecessary
Pressure fit may cause unwanted wear and tear over time.
Hard to Manufacture

## Slide 8: Prototype 2
The second concept:
Two-part aluminum legs
Holes for water flow
Threaded Legs
Silicone Leg Caps
Issues:
Straight Legs are not available for purchase
Difficult to put internal threads on HDPE

## Slide 9: Prototype 3
The third concept:
Foldable legs
Holes for water flow
Silicone Leg Caps
Pins to prevent rotation of the legs
Issues:
Straight legs are not available for purchase
Difficult to put internal threads on HDPE

## Slide 10: Prototype 3 Stress Analysis

## Slide 11: Feasibility
With Wix, a low skill web designing tool, we can finish the training web before the due date July 12
Because of the display-based advertising from Wix, there is no fee to web hosting. The University of Ottawa has Arduino tutorial videos that can be embedded into our website for instructional content.
There is no legal liability for the ads from our end because the ads are entirely managed by Wix.
Compared to the competition this website and all its features are free.

## Slide 12: BOM

## Slide 13: Business Model

## Slide 14: Economic Report (Income Statement)
Income Statement (All Numbers are in CAD) | Year 1 | Year 2 | Year 3
Sales | 800,000 | 1,500,000 | 2,250,000
Cost of Goods Sold | 200,000 | 500,000 | 750,000
Gross Profit on Sales | 400,000 | 1,000,000 | 1,500,000
Operating Expenses: |  |  | 
Marketing | 40,000 | 30,000 | 30,000
General Admin | 190,000 | 190,000 | 190,000
Overhead | 50,000 | 50,000 | 50,000
Labour | 240,000 | 300,000 | 380,000
Equipment Rental | 100,000 | 100,000 | 100,000
Total Operation Expenses | 620,000 | 670,000 | 750,000
Net Income | -220,000 | 330,000 | 750,000

## Slide 15: Economic Report (NPV)
Year | Cash Flow | NPV | Cumulative NPV
0 | -620,000 | -620,000 | -620,000
1 | -220,000 | -$200,000.00 | -820,000
2 | 330,000.00 | $272,727.27 | -547,273
3 | 750,000.00 | $563,486.10 | 16,213

## Slide 16: Decisions Made
Use discord to communicate
Update on existing products
Height-adjustment system(silicones)
Use ABS as materials
3D printing & milling

## Slide 17: Trials and Tribulations
Insufficient funding for the acquisition of materials and too slow shipping
Poor time management by the group during exam week
3D printing failure rate is too high to get a satisfactory product

## Slide 18: Lessons Learned
Teamwork is the most significant thing during the whole design
Focus more on learning skills instead of the result
Take precautions and prepare to deal with all kinds of reactions
Be a good listener and collect feedback from anyone

## Slide 19: Project Plan

## Slide 20: Future Work
Avoid time conflicts and distribution unbalanced
Improvement needed on 3D print skills

## Slide 21: Conclusion