## Slide 1: C1.1
Communication Pointer Mounting

## Slide 2: Client vs Customer
Computer Wise
  Not-for-profit organization
  Improve lives of people with multiple disability using technology
People in the following demographic
  Limited speech ability
  Uses bliss board
  Limited hand mobility
Notes: First let us look at our client and our customer. Our client is not-for-profit organization called Computer Wise. They try to improve the lives of people with multiple disability using technology.
Our clients would be people who have use bliss board, but have limited hand mobility

## Slide 3: Bliss Board
Communication Board
  For non-verbal/speech impaired people
  Point to elements using hands
  Can be simple (pictures) or complex (words)
Notes: But what is bliss board you might ask? Bliss board is a communication board used by non-veral or speech imparied people. People can point to the elements on the board using their fingers to communicate with others. The elements can be either words or complex words.

## Slide 4: Client Needs
Need # | Need | Importance
1 | The product is a hands-free device | 4
2 | The laser can be reliably turned on and off without the use of arms and hands | 5
4 | The mount allows controlled and steady movement of the laser pointer | 4
7 | Mount allows attachment to the temples of the glasses | 5
9 | Batteries are easily replaced/recharged | 4
19 | The product stays true to what the customer suggested | 5
Notes: Moving on to the product. Essentially, our client wants us to develop a way to help their customers use bliss board using their head. This means mounting a laser pointer to their glasses. The pointer should be turned on and off using their head as well.

## Slide 5: Benchmarking
Bridges Canada
Low Tech Solutions
Too Expensive! ~$300CAD
No head activated switch
Notes: We found two companies that sold similar looking products. They were both too expensive and no head activated switch.

## Slide 6: Target Specifications
Metric | Target | Unit
Laser Stability | 5 | cm
Battery Life | 10 | hr
Hands-free activation | Y | Y/N
Activation sensitivity (error rate) | 15 | %
Laser beam visibility | 2m indoors | # of environments
Time to detach | 30 | s
Notes: These are some of the important target specs that our final product needs to meet. Aidan will cover the ones related to Prototype 1 later.

## Slide 7: Three Possible Concepts
Concept #1
Simple
Light weight on glasses
Ease of production
Hip mounted: Battery (Rechargeable USB power bank) and Arduino Nano
Frame Mounted (Either Side): Laser Diode and Accelerometer
Cable: Connects components on hip and frame
Add-On: Shirt Clip

## Slide 8: Three Possible Concepts
Concept #2
Left Frame Mounted: Rechargeable battery bank.
Right Frame Mounted: Arduino Nano, Laser Diode and Accelerometer.
Cable: Connects components on left and right frame.
No hinderance while moving head
Added weight to frames
Much smaller battery

## Slide 9: Three Possible Concepts
Concept #3
Frame Mounted (Either Side): Non-rechargeable button battery, Arduino Nano, Laser Diode and Accelerometer.
Cable: None. components soldered
All-in-one system
More complex design. Difficult to prototype and test
Non rechargeable button battery. Manually replaced

## Slide 10: Client Feedback
Concept 1 preferred by client (external battery pack)
User has less range of motion of the head than initially anticipated
Need of a physical power switch for staff
Discussed possibility of having an automatic timer based turn off system when motion is not detected

## Slide 11: Final Design – Mechanical System
Glasses mounted system
  Clips
  3D printed casing
    Laser, accelerometer, power button
Hip mounted battery pack
  Pouch
  Portable power bank
  3D casing
    Arduino

## Slide 12: Final Design – Electrical System
Circuit components: battery, Arduino Uno, accelerometer, laser diode, button, resistor
All components connected to Arduino
  Accelerometer connected to analog pins
  Laser diode and button connected to digital pins
Resistor used to allow button to act as if it is in high state when button not pressed

## Slide 13: Final Design – Software
While kill switch is disabled
  If movement is detected, laser is turned on
  After 4 minutes of no movement, the laser turns off
Enabling the kill switch at any point in time will interrupt the program and turn the laser off

## Slide 14
Item # | Item | Purchase location | Quantity | Price (CAD)
1 | Arduino Uno | MakerStore | 1 | 17.00/piece
2 | Accelerometer | Amazon | 1 | 15.89/3 pieces
3 | Laser | Petsmart | 1 | 5.99/piece
4 | Battery | Amazon | 1 | 22.99/piece
5 | Button | MakerStore | 1 | 5.00/20 pieces
6 | Wire | Makerspace | N/A | 0
7 | Solder | Makerspace | N/A | 0
8 | PLA | Makerspace | N/A | 0
9 | Clips | Amazon | 5+ | 14.29/30 pieces
10 | Adhesive | Makerspace | N/A | 0
11 | Pouch | Amazon | 1 | 14.99/piece
Total cost= |  |  |  | 96.15 + tax
Total cost by piece = |  |  |  | 68.90 + tax
Item # | Item | Purchase location | Quantity | Price (CAD)
1 | Arduino Uno | MakerStore | 1 | 17.00/piece
2 | Accelerometer | Amazon | 1 | 15.89/3 pieces
3 | Laser | Petsmart | 1 | 5.99/piece
5 | Button | MakerStore | 1 | 5.00/20 pieces
6 | Wire | Makerspace | N/A | 0
7 | Solder | Makerspace | N/A | 0
8 | PLA | Makerspace | N/A | 0
9 | Clips | Amazon | 5+ | 14.29/30 pieces
10 | Adhesive | Makerspace | N/A | 0
Total cost= |  |  |  | 58.17 +tax
Fully Functional Prototype:
Proof of concept prototype:
List of Parts and BOM

## Slide 15: Prototype 1
Notes: Isaac
Moving on to the content of Deliverable D

## Slide 16: What is Prototype 1
Analytical focused on the electrical and software components
Using TinkerCAD
Low cost, low fidelity
The original purpose was to test intended code and circuits for feasibility and remove bugs or errors before physical tests. Along with testing power draw to calculate expected battery life.
Several issues with TinkerCAD simulations prevent intended testing
Graph from Lecture Slide 07
Notes: Using some things mentioned during Thursday’s Design review we did an Analytical focused prototype related to the Electrical and Software components
On this graph presented during the lectures we are about here at this simulation aspect
Our prototype encountered some issues relating to the program we were using to simulate TinkerCAD, that I will go into
The intended goal was to simulate the circuit and code to identify and refine any errors before moving to a physical prototype, while due to suggestions from Thursday measure power draw of the circuit and how that might limit use

## Slide 17: Original circuit that would be tested
Issues
TinkerCAD would not allow direct or indirect analysis of power draw of Arduino
Accelerometer could not be completely simulated, allowing us to simulate motion to test code
Lasers are not an insertable component in TinkerCAD, approximated to LED
Notes: This was the original circuit we intended to test
TinkerCAD prevented us from measuring the power consumed by the Arduino
The accelerometer was not completely embedded in TinkerCAD so we could simulate power draw but not function, allowing us to get readings
No laser component, we approximated to an LED, which not have the same power consumption

## Slide 18: Final Version Prototype 1
ATTINY in place of Arduino to measure power draw
Potentiometer inserted to provide input to code in place of accelerometer
Laser still approximated to LED that will have a lower power draw
Notes: Arduino is replaced with an ATTINY microcontroller, which we can still code but can measure power consumption
Accelerometer was left in to measure power, but feedback was given using a potentiometer, allowing our code to be tested
This is now an idealized version of the final circuit in terms of power requirements, and will likely serve as a baseline for future tests with actual components
Code remains mostly unchanged allowing us to do basic error fixes and some tuning

## Slide 19: Final Tests Performed and Purpose
Using readouts in the simulation an ideal power draw can be calculated, from less power costly components
Test code concept and communicate code function
Refine code and circuit
Notes: As stated, some of the final tests and purposes of this prototype are to get a baseline power requirements of our product
Develop our code and more effectively demonstrate its function
Generally, refine how the circuit and code function

## Slide 20: Final Test Results: Power Calc
Power draw sim 40mW with 8.01mA current draw
Arduino uno idle power draw 400mW with 80mA current draw
Laser choice power draw: max power draw 5mW with max 1mA current draw
Total current Draw: 89.01 mA

## Slide 21: Final Test Results: Battery
Current draw range 89.01 - 200 mA (Max draw of Arduino)
Estimate battery life with 5000mAh batter: 25 - 56 Hrs
Estimate time to charge: 12 W output (5 V/2.4 A) 3-4Hrs

## Slide 22: Final Results vs Target Specs
Metric # | Need # | Metric | Target/Expected | Simulation Results | Unit
1 | 9 | Time to charge | 4 | 3.5 | h
5 | 12, 15 | Laser beam range | 2 | 1.83 (6ft) | m
6 | 11 | Laser safety grade | Class II | Class II | class
 |  | Cost | 50 | 96.14 | $
10 | 10 | Battery life | 10 | 25 - 56.1 | h
11 | 13, 15 | Laser beam visibility | 2m indoors | 2m indoors, | # of environments
12 | 1, 2 | Hands-free activation | Y | Y | Y/N

## Slide 23: Live Demo