## Slide 1: Automated Punching System
Group Members: Tayyeb Juned momin
Kevin Xia
B M Adnan
Supervised By: Dr. David Bruce

## Slide 2: Table of contents
Process Flow
03
Q&A
06
Solution Overview
02
Future Work
05
Introduction
01
Features & Benefits
04

## Slide 3: Introduction
Problem:
Manual hole-punching in electroplating leads to misalignment, material waste, and inefficiencies. A single mistake can result in costly rework.
Solution:
Our Automated Punching System ensures pinpoint accuracy, speed, and cost savings—removing human error and streamlining production.

## Slide 4: Solution Overview
The system features a user-friendly digital interface where designs are easily uploaded, and the automated process ensures consistent, accurate punching with minimal human intervention.

## Slide 5: Process Flow
Upload Design
Material Setup
Punching
Removal

## Slide 6: Upload Design
Design the required pattern
Upload the pattern onto the software interface
The software would convert the design input to punch instructions

## Slide 7: Material Setup
Apply the film on the template
Attach the template onto the printer bed

## Slide 8: Punching Setup (Currently Tried)
Attach the punch to designed tool head instead of the extruder head on the printer. Using this punch try to push it through the film. There was no hole created instead it peeled off the film from the template.
Tried using a 20N (rated) solenoid to generate the force. The punch force was not enough to punch through.
Direct Punch
Solenoid

## Slide 9: Punching Setup (Future Work)
Using a laser module to cut the holes in the polyimide film. The problem with this approach could be the edges of the holes won’t be clean instead would have burrs on it.
Using a much more powerful Solenoid to punch through. The issue with this setup would be the expense and effeciency.
Using the existing solenoid with a lever system to generate the required force. The challenge would be to set it up on a 3d printer.
Laser
Powerful Solenoid
Lever System

## Slide 10: Removal
Apply the nickel substrate on the polyimide film
Remove the combination from the template
Detach the template from the printer

## Slide 11
Automated Punching Mechanism
User-Friendly Software Interface
Customizable Punching Parameters
High Repeatability & Consistency
Reduces Material Waste
Increases Production Efficiency
Minimizes Human Effort
Cost-Effective
Improved Electroplating Quality
Features
Benefits

## Slide 12: Future Work
Better punching/cutting mechanism
Automate the alignment process
Eliminate the need for template
Eliminate the need to upload the design instead include the designing in the software interface itself
Work on safety features

## Slide 13: Thanks
Do you have any questions?