## Slide 1
In the nuclear sector, high radiation levels and unsafe environments present challenges when retrieving metal samples from nuclear equipment. Extended exposure to these hazardous conditions during nuclear infrastructure evaluation poses significant health risks to humans.
Problem
Design Goal and Requirements
Determine key features to focus on
Design and build the three main subsystems: locking, scraping / collection, and push / pull
Program the microcontroller in C/C# (Arduino) to control servos and BLDCs using sensor feedback
Create a user interface that the operator can use with the system
Enable the system to send status updates back to the operator
Adjust the program and design as needed to boost reliability and performance
Design Process
The most unique part of our design is its locking mechanism. After many rounds of testing and tweaking the precisely made parts, we built a system that lets our rotating scraper run at high speeds to get the most out of its efficiency. In our first design, the linkages and center disk didn’t have bearings, but testing showed us that adding them was necessary for smoother operation. With the bearings in place, the large servo can push fully against the pressure tube walls instead of wasting energy on friction, making everything work better. This improvement not only makes the motor run more smoothly, but it also reduces wear and tear, helping the whole system last longer and perform reliably even under heavy use.
Custom In-House Designed Locking Mechanism
Testing revealed the maximum force the locking mechanism can sustain
Sample amounts varied based on the scraping mechanism’s rotation time and speed
Dual collection chambers allowed two samples to be taken in one trial, boosting efficiency
A movement system guided by a measuring tape allowed precise positioning before the locking mechanism engaged
Conclusion
The tool efficiently reaches the desired depth, collects two separate samples, and returns to the operator
The device is failsafe and can be retrieved at any point during the collection process
The user interface is simple and provides active feedback to the operator
Bibliography and extra resources can be found in research binder.
All photographs, diagrams and charts were generated by the research team.
A BLDC motor differs from traditional DC motors by using an electronic system to switch the magnetic field controlling the commutator, rather than relying on brushes that physically contact and switch the magnetic orientation.
Revolutionizing Hazardous Nuclear Sampling: Advanced Robotics for High-Radiation Metal Sampling and Infrastructure Assessments
Future Designs
Future designs would:
Use LiDAR to determine the precise position of the design within the pressure tube
Implement a custom lithium battery system to reduce dependence on external battery or power
Add a second lock and a method to seal the scraper so no particles are loose in the pressure tube
Design’s Use of BLDC Motors
The goal was to develop a solution that can safely retrieve a 30-80 mg metal sample of Zirconium from 15 feet inside of a pressure tube with a 4-inch inner diameter.
The device needs to have a fail safe function for retrieval of sample and robot in case of failure.
The system must be able to communicate its status to the operator with an interface.
The device must contain the sample after collection.
The device should be portable and modular for repair.
Discussion
Software/Hardware Needed
C/C# to program microcontroller and Processing to create the user interface that reflects the device status
Encoder and diametric magnet from the BLDC provide angle and speed of scraping and collection system
Brushless motor and slip ring to allow rotation of mechanism at high speed while maintaining communication
Metal geared servos to control locking mechanism and collection system
Battery that lasts long enough to conduct multiple trials
Component Evaluation
Background research identified expensive alternatives that were too large to fit in the pressure tube or lacked tooling to collect Zirconium samples.
Sampling solid Zirconium requires either speed, strength, or a combination of both.
Closed / Unlocked State
Image of how a simple BLDC (BrushLess Direct Current) uses electromagnets on the stator to rotate the permanent magnet commutator
Processing links with Arduino IDE and microcontroller
Scraping and Collection Mechanism:
Actuated joint extends scraper and collection mechanism to tube walls
Scrapes tube wall and collects material on following pass around
2 servos control scraper distance
BLDC rotates mechanism at 150 RPM
Slip ring allows wires to be rotated
Component | Purpose | Alternatives
Locking Mechanism | Hold entire system in place during scraping | Spring
Movement Mechanism | Transport device in and out of the pipe with precision and speed | Motorized Wheels
Scraping Mechanism | Obtain and collect metal sample by scraping the inside layer of the pipe | Brush System
Brushless and Servo Motors | Controls movement of system, turning of scrapers, and extending the arms of locks | Stepper Motors
ESP-32 S3 | Controls commands for everything that needs instructions | Arduino Uno
Digital Interface | Provides the user with feedback | Cameras
Brushless motors also have the advantage of precise control, reduced maintenance, a longer lifespan, and quieter operation, making them ideal for applications that demand both performance and reliability.
CAD Design
Realized Prototype
Open / Locked State
Closed / Unlocked State
Open / Locked State
Servos x 2
BLDC & Slip Ring
Push / Pull Mechanism:
Rigid off the shelf measuring tape as starting point of design
Pushes and retracts the device in and out of the pressure tube
Operates in both horizontal and vertical orientations
Software and Electronic Design:
Programmed in C/C# (Arduino)
2 x Micro Servo and 1 x Large Servo
2 x BLDC
1 x ESP32 Microcontroller
1 x Encoder & Diametric Magnet
See Resources for complete code & Bill Of Materials
Lock Mechanism
Push / Pull Mechanism
Collect / Scrape Mechanism